## Slide 1: UMBRA NBS
Product | KuroLok Roller Shades, detachable crank
Manufacturer | Umbra
Web | www.umbrashading.co.uk
Tel | 01792 562015
Install | Products to be installed by Umbra approved installers only. Call Harry Doling on 01792 562015 to get the details for your approved local installer.
Type | Heavy duty cassetted roller blind system with zipped edge fabric retention in side channels
Operation | Magnetic detachable crank handle - inherently complies with standard BS EN 13120 child safety standard.
Hardware colour | White RAL 9016 or Black RAL 9005
Fabric | Spectrum 5010 3% screen fabric for dimout or Spectrum 1010 contract PVC blackout fabric for room darkening
Fabric finish/colour | TBC.
Accessories |
- 93mm x 100mm aluminium cassette profile with front cover removeable within 100mm pocket
- 35mm x 24mm aluminium side channel
Size | TBC. [max 4.0mW, 6.0mD; 14m2]
Warranty | 12 years