## Slide 1: UMBRA NBS
Product | Sirios Roller Shades with cassette and side channels, fixed crank
Manufacturer | Umbra
Web | www.umbrashading.co.uk
Tel | 01792 562015
Install | Products to be installed by Umbra approved installers only. Call Harry Doling on 01792 562015 to get the details for your approved local installer.
Type | Heavy duty roller blind system with cassette and side channels
Operation | Fixed crank handle - inherently complies with standard BS EN 13120 child safety standard.
Hardware colour | White RAL 9016
Fabric | Spectrum 5010 3% screen fabric for dimout or Spectrum 1010 contract PVC blackout fabric for room darkening
Fabric finish/colour | TBC.
Accessories |
- 20mm diameter aluminium hembar - RAL 9016
- 78.5mm x 78mm round cassette headbox – RAL 9016
- 46mm x 26mm side channel – RAL 9016
Size | TBC. [max 3.0mW, 3.0mD; 6m2]
Warranty | 7 years